## Slide 1: XFabric: a Reconfigurable In-Rack Network for Rack-Scale Computers
Sergey Legtchenko, Nicholas Chen, Daniel Cletheroe, Antony Rowstron, Hugh Williams, Xiaohan Zhao

## Slide 2: Increasing Performance per $ in Data Centers
Hardware designed for data centers
Racks as units of deployment & operation
Google Jupiter
(data center fabric)
Pelican
Cold Storage
SoC
CPU
NIC/Packet switch
d ports
Controllers: IO, memory...
Systems on Chip (SoCs)
Rack scale computer
e.g. Boston Viridis
Server = Calxeda SoC
900 (wimpy) CPUs
80 servers
160 CPUs
Open CloudServer (OCS) rack
Standard rack
40 servers
80 CPUs
In-rack consolidation
$$$/server
$/server

## Slide 3: In-rack Networks for Rack-Scale Computers
Challenge: reducing in-rack network cost
Full bisection bandwidth: 9 Tbps
Cost: $$$$$
900 ports
Multi-tiered?
High power draw/cost
>900 ports
ToR switch?
Direct connect topology
(e.g. mesh)
SoCs with packet switches
Low cost
Oversubscribed
d ports/SoC
Rack scale computer
e.g. Boston Viridis
Server = Calxeda SoC
900 (wimpy) CPUs

## Slide 4: Oversubscription in Direct-Connect Topologies
SoC A
CPU
Packet
switch
SoC C
CPU
Packet
switch
SoC B
CPU
Packet
switch
SoC D
CPU
Packet
switch
Multi-hop routing
Path length impacts performance
  Higher, less predictable latency
  Lower goodput
…
…
…
…
A->D
Example: 3D Torus with 512 SoCs
  Average hop count = 6
  6x oversubscription
Path length is low if the topology is adapted to traffic

## Slide 5: XFabric: a Reconfigurable Topology
SoC A
CPU
Packet
switch
SoC C
CPU
Packet
switch
SoC B
CPU
Packet
switch
SoC D
CPU
Packet
switch
…
…
…
…
Rack
Adapting topology to traffic
  Lower path length
  Reduced oversubscription

## Slide 6: XFabric: a Reconfigurable Topology
SoC A
CPU
Packet
switch
SoC C
CPU
Packet
switch
SoC B
CPU
Packet
switch
SoC D
CPU
Packet
switch
…
…
…
…
Rack
Adapting topology to traffic
  Lower path length
  Reduced oversubscription
Circuit switched fabric
  Electrical signal forwarding
  No queuing, no packet inspection
Physical circuit

## Slide 7: XFabric: a Reconfigurable Topology
SoC A
CPU
Packet
switch
SoC C
CPU
Packet
switch
SoC B
CPU
Packet
switch
SoC D
CPU
Packet
switch
…
…
…
…
Rack
Adapting topology to traffic
  Lower path length
  Reduced oversubscription
Circuit switched fabric
  Electrical signal forwarding
  No queuing, no packet inspection
A->D

## Slide 8: XFabric: a Reconfigurable Topology
SoC A
CPU
Packet
switch
SoC C
CPU
Packet
switch
SoC B
CPU
Packet
switch
SoC D
CPU
Packet
switch
…
…
…
…
Rack
Adapting topology to traffic
  Lower path length
  Reduced oversubscription
Circuit switched fabric
  Electrical signal forwarding
  No queuing, no packet inspection
A->D

## Slide 9: XFabric Architecture
SoC A
CPU
Packet
switch
SoC C
CPU
Packet
switch
SoC B
CPU
Packet
switch
SoC D
CPU
Packet
switch
…
…
…
…
Rack
Uplinks
Controller
(process on one SoC in the rack)
Generate topology
Minimize path length
Configure data plane
Assign circuits
Update SoC routing
Estimate
demand
Control plane
Periodic topology reconfiguration
Dynamic uplink placement
Data center aggregation switch

## Slide 10: Circuit-Switching Fabric Cost
SoC A
CPU
Packet
switch
SoC C
CPU
Packet
switch
SoC B
CPU
Packet
switch
SoC D
CPU
Packet
switch
…
…
…
…
Rack
Challenge: high port count
  Too high port count for one ASIC
Commodity ASICs
  160 ports @ 10 Gbps
  Max size: ~350 ports
Cost : $3/port
e.g. 300 SoCs, 6 ports/SoC: 1,800 ports

## Slide 11: Circuit-Switching Fabric Cost
SoC A
CPU
Packet
switch
SoC C
CPU
Packet
switch
SoC B
CPU
Packet
switch
SoC D
CPU
Packet
switch
…
…
…
…
Rack
Challenge: high port count
  Too high port count for one ASIC
  Folded Clos total cost: $27K
Commodity ASICs
  160 ports @ 10 Gbps
  Max size: ~350 ports
Cost : $3/port
e.g. 300 SoCs, 6 ports/SoC: 1,800 ports
x30 300 port ASICs

## Slide 12: Reducing Circuit-Switching Fabric Cost
SoC A
CPU
Packet
switch
SoC C
CPU
Packet
switch
SoC B
CPU
Packet
switch
SoC D
CPU
Packet
switch
…
…
…
…
Rack
Trading off reconfigurability for cost
Full reconfigurability:
  Any 2 ports can be connected

## Slide 13: Reducing Circuit-Switching Fabric Cost
SoC A
CPU
Packet
switch
SoC C
CPU
Packet
switch
SoC B
CPU
Packet
switch
SoC D
CPU
Packet
switch
…
…
…
…
Rack
Trading off reconfigurability for cost
Full reconfigurability:
  Any 2 ports can be connected
Partial reconfigurability:
  Port can connected to subset of ports

## Slide 14: Reducing Circuit-Switching Fabric Cost
SoC A
CPU
Packet
switch
SoC C
CPU
Packet
switch
SoC B
CPU
Packet
switch
SoC D
CPU
Packet
switch
…
…
…
…
Rack
Connected to port 0
on all SoCs
…
Connected to port N
on all SoCs
Trading off reconfigurability for cost
Full reconfigurability:
  Any 2 ports can be connected
Partial reconfigurability:
  Port can connected to subset of ports

## Slide 15: Reducing Circuit-Switching Fabric Cost
SoC A
CPU
Packet
switch
SoC C
CPU
Packet
switch
SoC B
CPU
Packet
switch
SoC D
CPU
Packet
switch
…
…
…
…
Rack
…
Trading off reconfigurability for cost
Full reconfigurability:
  Any 2 ports can be connected
Partial reconfigurability:
  Port can connected to subset of ports
  x5 Lower cost compared to full reconfigurability: $5.4K
x6 300-port ASICs

## Slide 16: XFabric Performance at Rack Scale
Flow-based simulation, 343 SoCs, 6 ports/SoC

## Slide 17: XFabric Performance at Rack Scale
Flow-based simulation, 343 SoCs, 6 ports/SoC
Varying traffic skew
Chart: Skew (cluster size)
| 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 344
3D Torus | 5.1793 | 5.1583 | 5.199 | 5.1606 | 5.1306 | 5.1449 | 5.1423 | 5.1283 | 5.1793
Random | 3.5208 | 3.5182 | 3.5087 | 3.5175 | 3.5266 | 3.5255 | 3.5177 | 3.5583 | 3.5175
XFabric | 1 | 1.031 | 1.3198 | 1.7009 | 2.0636 | 2.5408 | 3.0566 | 3.4847 | 3.5575
Fully reconfigurable | 1 | 1 | 1.2093 | 1.6915 | 2.3533 | 2.6359 | 2.8831 | 3.2636 | 3.5636
Skewed
Uniform
(7x7x7)

## Slide 18: XFabric Performance at Rack Scale
Flow-based simulation, 343 SoCs, 6 ports/SoC
Varying traffic skew
Production cluster workload
  Traffic matrix from TCP flow trace
Chart: 
| Production
3DTorus | 5.9266
Random | 3.5165
XFabric | 1.0643
Fully reconfigurable | 1.064
Chart: Skew (cluster size)
| 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 344
3D Torus | 5.1793 | 5.1583 | 5.199 | 5.1606 | 5.1306 | 5.1449 | 5.1423 | 5.1283 | 5.1793
Random | 3.5208 | 3.5182 | 3.5087 | 3.5175 | 3.5266 | 3.5255 | 3.5177 | 3.5583 | 3.5175
XFabric | 1 | 1.031 | 1.3198 | 1.7009 | 2.0636 | 2.5408 | 3.0566 | 3.4847 | 3.5575
Fully reconfigurable | 1 | 1 | 1.2093 | 1.6915 | 2.3533 | 2.6359 | 2.8831 | 3.2636 | 3.5636
Lower is
better
Path length (#hops)
Skewed
Uniform
(7x7x7)
(7x7x7)

## Slide 19: XFabric Prototype Performance
XFabric prototype
  SoC emulated by server
Gen2: 160 ports @ 10Gbps
Server
Software
Packet Switch
Filter driver
Application
6 NICs
Gen1: 32 ports @ 1Gbps
  27 servers
  Unmodified TCP/IP applications
  6 circuit switches, custom PCB design

## Slide 20: XFabric Prototype Performance
XFabric prototype
  SoC emulated by server
  27 servers
  Unmodified TCP/IP applications
  6 circuit switches, custom PCB design
Gen1: 32 ports @ 1Gbps
Gen2: 160 ports @ 10Gbps
Server
Software
Packet Switch
Filter driver
Application
6 NICs
Chart: 
| 480 | 240 | 120 | 60 | 30 | 10 | 1 | 0.1
XFabric | 1 | 0.96904 | 0.95422 | 0.90572 | 0.85458 | 0.81073 | 0.7885 | 0.82604
23% improvement
3DTorus
Completion time
(normalized to 3DTorus)
Reconfiguration period (sec)

## Slide 21: Conclusion
Rack-Scale Computers
  Higher performance per $
  Up to hundreds of SoCs/rack
XFabric: in-rack network with reconfigurable topology
  Dynamic adaptation to traffic demand
  Low cost
Deploying new circuit switch hardware
  Electrical circuit switching, 160 ports @ 10Gbps